## Slide 1: Acoustics of Speech and Linear Prediction Modeling
EE6641 Analysis and Synthesis of Audio Signals
Yi-Wen Liu
Updated Nov. 24, 2015

## Slide 2: Agenda
Acoustics
  Impedance, reflectance, multi-tube modeling
Linear prediction (LP)
  Relation to acoustics
  LP and spectral analysis
    Least-square formulation
    Formants: resonant peaks
  LP and speech synthesis
  LP and speech recognition

## Slide 3: Acoustics: the impedance concept
Canonical acoustic variables are
  Acoustic pressure P(x,t)
  Volume velocity U(x,t)
  Z = P/U is the characteristic impedance
  (and, how about Q = PU?)
  Based on continuity and Newton’s law, Z = rc/A
    r: Density of air
    c: Speed of sound (~340 m/s or 1 ft/ms)
    A: Cross-section area

## Slide 4: More on Z = rc/A
The characteristic impedance is frequency-independent (?!)
This formula does not consider
  Dissipative loss
    Friction 摩擦力
    Viscosity 黏滯性
  Propagation modes
  Turbulence 紊流
  Other nonlinear effects

## Slide 5: Continuity, impedance mismatch, and acoustic reflectance
Now consider acoustic wave propagation through the boundary between two tubes
Due to impedance mismatch, a portion of the wave is reflected and a portion crosses the boundary
P1+
P2+
P1-

## Slide 6: Acoustic pressure reflectance and transmittance
Reflectance R can be defined as P1-/P1+
Based on continuity, we can show that
  r12 = (Z1-Z2)/(Z1+Z2)
  T = 1-r is called the transmittance
P1+
P2+
P1-

## Slide 7: Two-port formulation
Now consider reflected waves as a linear combination of left- and right- going incident waves
  use volume velocity U as the input-output variable
U1+
U2+
U1-
U2-
we have:
7

## Slide 8: Signal-flow graph
u1+[n]
u1-[n]
u2+[n]
u2-[n]
1+r
-r
r
1-r
U1+
U2+
U1-
U2-

## Slide 9: The multi-tube model of the vocal tract
This part changes its
shape when producing
speech
Z1
Z2
ZN
r12
r23
rN-1,N
. . .
Zi: char. impedances
rij : reflectances
http://cobweb.ecn.purdue.edu/~ee649/notes/figures/vocal_schematic.gif

## Slide 10: Signal flow of the multi-tube model
Z1
Z2
ZN
r12
r23
rN-1,N
. . .
u1+[n]
u1-[n]
u2+[n]
u2-[n]
1+r12
-r12
r12
1-r12
t2
t2
u3+[n]
u3-[n]
1+r23
-r23
r23
1-r23
t3
t3
and so on…

## Slide 11: Source modeling
u1+[n]
u1-[n]
u2+[n]
u2-[n]
1+r12
-r12
r12
1-r12
t2
t2
u3+[n]
u3-[n]
1+r23
-r23
r23
1-r23
t3
t3
and so on…
Source impedance:
Source Reflectance:
uG[n]
volume
velocity
at glottis
u1+[n]
u2+[n]
1+r12
-r12
r12
1-r12
t2
…
t1
t1
(1+rG)/2
rG

## Slide 12: Load modeling
Load impedance due to radiation from lips:
uN+[n]
1+rN-1
-rN-1,N
rN-1,N
1-rN-1,N
tN
…
tN
Load reflectance:
-rN
1+rN
Frequency-dependence analysis:
Frequency decrease
=> Zr approaches 0 => rN approaches 1,
which means output acoustic pressure approaches 0.
Frequency increases
=> rN approaches a constant.

## Slide 13: The entire multi-tube model with source and load
uin[n]
volume
velocity
at glottis
uout[n]
Radiation from lips
Z1
Z2
ZN
r12
r23
rN-1,N
. . .
1+r12
-r12
r12
1-r12
t2
t1
t1
(1+rG)/2
rG
1+rN-1
-rN-1,N
rN-1,N
1-rN-1,N
tN
…
tN
-rN
1+rN
…
t2

## Slide 14: Linear prediction: Vocal tract as an all-pole IIR filter
e[n]
glottal source;
excitation
x[n]
output
We can write x[n] in terms of e[n]:
This equation is called a linear prediction model
P is the order of prediction
ak’s are the linear prediction coefficients

## Slide 15: Speech analysis and synthesis based on LP
Analysis:
  record x[n]
  estimate ak’s that gives best prediction of x[n]
  Best prediction is formulated as a least-square problem*
Synthesis: Create e[n], synthesize x[n] in real-time.
  Reflectances and LP coefficients are related via the Levinson-Durbin recursive formula.
glottal source;
excitation
e[n]
output
x[n]

## Slide 16: LP analysis: a least-square formulation
Find {ak}, k = 1, 2, …, P
so as to minimize the sum of square of prediction error e[n], defined as below,
Can be formulated as a matrix
inverse problem:
x[1] x[2] … … x[P]
x[2] x[3] … … x[P+1]
.
.
.
x[L] x[L+1] … x[P+L]
a1
a2
.
.
.
aP
≈
x[P+1]
x[P+2]
.
.
.
x[P+L]
K
a
b
Solution:
a = (KTK)-1(KTb)

## Slide 17: A least-square solver: MATLAB lpc() function
LPC Linear Predictor Coefficients.
A = LPC(X,N) finds the coefficients,
A=[ 1 A(2) ... A(N+1) ], of an Nth order forward linear predictor.
Xp(n) = -A(2)*X(n-1) - A(3)*X(n-2) - ... - A(N+1)*X(n-N)
such that the sum of the squares of the errors
err(n) = X(n) - Xp(n)
is minimized.

## Slide 18: Remarks on least-square prediction
The resulting prediction error e[n] is spectrally maximally flat
  The prediction “whitens” the signal
  Makes sense, for the white noise is uncorrelated from sample to sample, which makes it impossible to predict further.
In practice, because of spectral roll-off, one needs to pre-emphasize* before LP analysis.

## Slide 19: Pre-emphasis and de-emphasis
FIR pre-emphasis
y[n]
Linear Prediction
Analysis
x[n]
e[n]: estimated source
x[n] = y[n] – 0.95 y[n-1]
Multi-tube synthesis
e[n]
IIR De-emphasis
x[n]
y[n]
y[n] = 0.95 y[n-1] + x[n]
find {a1, … aP}

## Slide 20: Source-filter separation
Find {a1,..aP} such that energy of e[n] is minimized.
  Turns out that such e[n] will be maximally spectrally flat.
This provides a source-filter separation:
  {a1,..aP}: vocal-tract filter
  e[n]: glottal source = {voiced, unvoiced}
    When voiced, use pulse train
    When unvoiced, use white noise
All-pole filter {a1,..aP}
e[n]
Glottal
source
s[n]
Speech signal
Vocal tract
Noise generator
Pulse-train generator

## Slide 21: More on LP
Speech synthesis: By replacing e[n] with a template, speech compression achieves <8k bits/s.
  Codebook excited linear prediction (CELP)
  key technology for voice over internet and wireless networks.
Speech recognition: From {a1,..aP}, we can estimate
  Vocal tract constriction
  Frequency-envelope; formant structure.
All-pole filter {a1,..aP}
e[n]
Glottal
source
s[n]
Speech signal
Vocal tract

## Slide 22
All-pole filter {a1,..aP}
e[n]
Glottal
source
x[n]
x[n]
e[n]
X(ω)
E(ω)
Adapted from Rabiner & Juang, p. 108.
LP finds an all-pole filter that provides spectral smoothing

## Slide 23: Formant frequencies and speech production
f1
f3
f2
The formant filter
f2-f1
f1
300
900 Hz
300
2000
i (heed)
ɪ (hid)
ɛ (head)
ɑ (lot)
ɔ (law)
ʊ (look)
u (loose)
(had)
Articulation
space
front
back
high
low

## Slide 24: References
王小川: 語音訊號處理(三版, 2009) 全華出版社
S. Vaseghi (2007). Multimedia signal processing: theory and applications in speech, music, and communications. London: Wiley.
T. Quatieri (2001). Discrete-time speech signal processing: principles and practice. Prentice-Hall.
L. Rabiner and B.-H. Juang. (1993). Fundamentals of speech recognition. Prentice-Hall.