## Slide 1: Sinusoidal modeling
EE6641 Analysis and Synthesis of Audio Signals
Yi-Wen Liu
Nov 3, 2015

## Slide 2: Last time: Spectral Estimation
Resolution
  Scenario: multiple peaks in the spectrum
  Choice of window type and window length
  Rule of thumb: Dw = O(1/Dt)
Accuracy
  Scenario: signal in noise
  Quadratic interpolation of FFT log-magnitude
  Fisher Information and Cramer-Rao lower bounds
  Coherent frequency estimation: Dw = O(Dt-3/2)

## Slide 3: Today’s agenda
Sinusoidal modeling
  Analysis
    Formula for QI-FFT
    Choice of window
    Peak tracking
  Synthesis
  Applications
Spectral decomposition
  (S + N) vs. (S + N + T)
  Spectral subtraction

## Slide 4: QI-FFT: a fast frequency estimator
Windowing: time-domain multiplication with a shaping function
Zero-padding: append zeros in time  interpolate in frequency
FFT: apply fast Fourier transform
Peak detection: find every peak
Quadratic interpolation: fit a parabola in log-magnitude
The location of the parabola is the frequency estimate.
Reference: M. Abe and J. Smith, “Design criteria for simple sinusoidal parameter estimation based on quadratic interpolation of FFT magnitude peaks”, (AES 2004)
Hz
dB

## Slide 5: A formula for QI-FFT
-1
0
1
k
dB

## Slide 6: Example: finding peaks in a spectrum
Peaks can move
Peaks can grow or attenuate
Need to ignore side lobes
  But how?

## Slide 7: Blackman window has > 50 dB side-lobe suppression
All side lobes beneath the masking threshold.

## Slide 8: Example: Hann-windowed transform of trumpet sounds
Masked region
signal spectrum
Hz

## Slide 9: Psychoacoustic masking
Masking refers to the fact that softer sounds cannot be heard due to the presence of stronger sounds.
  Forward masking
  Simultaneous
  Backward masking
We will cover psychoacoustics later in this semester.

## Slide 10: Sinusoidal Modeling: from discrete peaks to trajectories

## Slide 11: Trajectory formation
Basic peak tracking involves:
  Finding shortest link
  Resolving splits
Advanced technique includes
  Forbidding large jumps
  Transient detection
  Highest peak chooses first

## Slide 12: Frequency-trajectories of a speech signal, arrows indicate transient regions

## Slide 13: Part II: Synthesis
Sinusoidal modeling
  Analysis
  Synthesis
    Linear-interpolation
    Phase continuation
    A window-based synthesis method
Spectral decomposition
  (S + N) vs. (S + N + T)
  Spectral subtraction
  Noise modeling (Nov. 16, 23)

## Slide 14: Sinusoidal synthesis (ii): the linear interpolation method
……..an amplitude envelope
……..a frequency envelope
Am
Am+1
A[n]
Remark: amplitude can be log
or linear scale.

## Slide 15: The linear-interpolation method (cont’d)

## Slide 16: From one trajectory to a signal: a window-based method
……..an amplitude envelope
……..a frequency envelope
Synthesis:
Continuous phase updates:
time
hT
Am

## Slide 17: summation over all trajectories
time
hT
Am

## Slide 18: Applications of sinusoidal modeling
Noise removal/ speech enhancement
  Potentials in hearing aids/ cochlear implants
Musical effects:
  Pitch shifting/ time warping
Parametric audio coding:
  MPEG-4 structured audio
  B. Vercoe et al. (1998). “Structured audio: Creation, transmission, and rendering of parametric sound representations,” Proc. IEEE, Vol. 86, No. 5, 922-40.

## Slide 19: Part III: Spectral decomposition
Sinusoidal modeling
  Analysis
  Synthesis
    Linear-interpolation
    Phase continuation
    A window-based synthesis method
Signal decomposition
  Spectral subtraction
  (S + N) vs. (S + N + T)
  Noise modeling (Possible final project idea)

## Slide 20: Example: a watermarking system based on signal decomposition (Liu & Smith, 2007)

## Slide 21: Sines + Noise + Transient (S+N+T) decomposition
Sinsusoids

## Slide 22: Spectral subtraction
For each peak in the spectrum, do
  fit the mainlobe of Blackman window
  subtract the mainlobe
  Inverse FFT to synthesis the residual (“noise”)

## Slide 23: Sines + “noise” decomposition by spectral subtraction
(a) Trumpet
(b) Dance music
Signal
Signal
Residual
Residual
0
2k
4k
6k
8k
10k
(Hz)
0
2k
4k
6k
8k
10k
(Hz)
Signal
Residual
100
(dB)
80
60
40
20
Parametric noise modeling?

## Slide 24: Transient detection
Sinsusoids

## Slide 25: Transient detection: there’s no gold standard
The following is just a heuristic approach
  Energy comparison
  Sine-to-residual ratio (SRR)

## Slide 26: Entering and exiting the transients
Once a transient is detected, sinusoidal model is halted for a period of time.

## Slide 27: Possible project ideas
Trajectory formation
  Causal implementation for real-time applications
Applications of spectral subtraction
  Noise-removal / Speech enhancement
Audio recognition
  Sound source segregation
  Audio fingerprinting/ watermarking
  And so on…