## Slide 1: Introduction to digital Audio Signals
EE6641 Analysis and Synthesis of Audio Signals
Prof. Yi-Wen Liu
Sep. 15, 2015

## Slide 2: What is digital audio about?
D/A
any transform (analysis)
and
processing (synthesis) you can think of
A/D
x(t)
Physical world
x[n]
y[n]
y(t)
“sampling frequency”
“sampling frequency”
Notes: Applications: (1) Effects (2) Coding

## Slide 3: Sampling: To look at the waveform at discrete-time
Taken care by your soundcard with the “input”
Need to specify how often you want to sample
The unit of sampling rate = Hz.
D/A
x(t)
Physical world
x[n]
“sampling frequency”

## Slide 4
Notes: 眯眯眼
40 samples in 1/200 sec. So sampling rate = ?
Conceptually, blue is continuous time. Red are its samples.
Question: How often do we need to sample?

## Slide 5: Undersampling

## Slide 6: Nyquist theorem
Need to sample at least at 2x the rate of the highest frequency of interest.
E.g., fs = 44.1 kHz for CD quality
Notes: As compared to 8 kHz for land-line telephone.
What if not sufficiently sampled?

## Slide 7: Quantization: fixed-point representation (usually)
D/A
x(t)
Physical world
x[n]
fs and nbits
A/D
y[n]
y(t)
fs and nbits
Physical world
Digital Domain
Nbits = 8, 16, 24, 32

## Slide 8: Quantization step D
Below are directly printed from MATLAB’s document for wavwrite()
NBits y Data Type Data Range Output Format
8 single or double –1.0 <= y < +1.0 uint8
16 single or double –1.0 <= y < +1.0 int16
24 single or double –1.0 <= y < +1.0 int32
32 single or double –1.0 <= y <= +1.0 single
重點: D = 2 / 2Nbits
Notes: 四捨五入解釋。
Q: Why 16 bits are sufficient for most applications?

## Slide 9: Analysis without synthesis: Machine listening
D/A
certain transform
x(t)
Physical world
x[n]
x: feature
“sampling frequency”
Machine Learning
Engines
Training data (optional)
Notes: Example: Speech recognition. 相關課程：Jeremy Lee

## Slide 10: Digital Sound Synthesis
Algorithm
or
Models
A/D
Parameters
y[n]
y(t)
“sampling frequency”
Controller
Notes: Example: Digital Instruments, 相關課程：交大聲創學程 黃志方教授，Max/MSP

## Slide 11: Demo of sound synthesis with a very specialized controller
Notes: Can stop at near 2:20.

## Slide 12: Related courses
李祈均教授：語音訊號處理
白明憲教授：聲學、陣列訊號處理
黃志方教授（交）：Max/MSP
冀泰石教授（交）：聽覺資訊處理